# Bell YOH-4

From Wikipedia, the free encyclopedia

Jump to navigationJump to search

| YHO-4 / YOH-4 |
| --- |
| YOH-4A LOH in flight |
| Role | Observation/scout helicopter |
| National origin | United States |
| Manufacturer | Bell Helicopter |
| First flight | 8 December 1962[1] |
| Primary user | United States Army |
| Number built | 5[2] |
| Variants | Bell 206A JetRanger |

The Bell YOH-4 (originally YHO-4) was a single-engine, single-rotor light helicopter, developed for the United States Army's Light Observation Helicopter program. While the YOH-4A was unsuccessful in the original LOH competition, Bell redesigned it as the sleek Bell 206A JetRanger for the commercial market, and enjoyed instant and lasting success. In 1967, the Army reopened the LOH competition, and the 206A-based OH-58 Kiowa was selected.

## Contents

- 1Development

- 2Variants

- 3Operators

- 4Surviving aircraft

- 5Specifications (OH-4A)

- 6See also

- 7References

- 8External links

## Development[edit]

On 14 October 1960, the United States Navy solicited responses from 25 aircraft manufacturers to a request for proposals (RFP) on behalf of the Army for the Light Observation Helicopter (LOH). Bell entered the competition along with 12 other manufacturers, including Hiller Aircraft and Hughes Tool Co., Aircraft Division.[3] In January 1961, Bell submitted Design 250 (D-250), which would eventually be designated as the YHO-4.[4] On 19 May 1961, Bell and Hiller were announced as winners of the design competition.[note 1][5]

YOH-4A LOH

Bell produced five prototypes of the D-250, as Model 206, in 1962, the first prototype making its maiden flight on 8 December 1962.[1] That same year, all aircraft began to be designated according to the new Joint Services designation system, so the prototype aircraft were redesignated YOH-4A.[1] The YOH-4A also became known as the Ugly Duckling in comparison to the other contending aircraft.[6] Following a flyoff of the Bell, Hughes and Fairchild-Hiller prototypes, the Hughes OH-6 was selected in May 1965.[7]

After the failed military contract bid, Bell attempted to market the Model 206, but it did not fare well commercially. Bell's market research showed that customers found the body design mostly unpalatable. Bell would eventually redesign the body of the airframe to a more sleek and aesthetic design and reintroduced it as the Bell 206A JetRanger.[8]

## Variants[edit]

OH-58 Kiowa

YHO-4

Bell 206 powered by a 250shp T63-A-5 for Army evaluation, five built later redesignated YOH-4A

YOH-4A

YHO-4s redesignated.

## Operators[edit]

United States

- United States Army

## Surviving aircraft[edit]

The remaining OH-4A 62-4202 is in storage at the Army Aviation Museum, Fort Rucker, Alabama.[9]

## Specifications (OH-4A)[edit]

Data from U.S. Army Aircraft Since 1947[2]

General characteristics

- Crew: one pilot

- Capacity: up to three passengers or two stretchers

- Length: 38 ft 8 in (11.79 m)

- Rotor diameter: 33 ft 3 in (10.13 m)

- Height: 8 ft 10 in (2.69 m)

- Empty weight: 1,536 lb (697 kg)

- Max. takeoff weight: 2,537 lb (1,150 kg)

- Powerplant: 1 × Allison T63-A-5 turboshaft, 250 shp (186 kW)

Performance

- Maximum speed: 117 knots (135 mph, 217 km/h)

- Cruise speed: 96 knots (111 mph, 179 km/h)

- Range: 246 nmi (283 mi, 455 km)

- Service ceiling: 20,000 ft (6,100 m)

## See also[edit]

- U.S. Helicopter Armament Subsystems

Related development

- Bell 206

- OH-58 Kiowa

Aircraft of comparable role, configuration and era

- Fairchild Hiller YOH-5

- OH-6 Cayuse

Related lists

- List of active United States military aircraft

## References[edit]

Notes

  - ^ The Navy, which was assisting the Army in the selection phase, recommended the Hiller Model 1100, while the Army team preferred the Bell D-250, and then the 1100. The Selection Board accepted both aircraft for an evaluation test. Afterwards, the acting Army Chief of Staff directed the Selection Board to include the Hughes 369 in the fly-off competition.